## Slide 1: Axillary Thermometer Proposal
Mobile Medical Devices
Team 3

## Slide 2: Mission Statement
“To create a reusable axillary (underarm) thermometer read-out system that wirelessly transmits body temperature data to an iPad which displays both instantaneous and average body temperature”
Keywords: axillary, underarm, body temperature, thermometer, read-out, wireless, iPad

## Slide 3: Top 10 Customer Requirements
(In no particular order)

## Slide 4: Accurate
Normal body temperature is 98.6 F, but 99 F is considered a low grade fever. Thus we need accuracy to be no less than +/- 0.1 F

## Slide 5: Ergonomic Thermometer
It should be very intuitive for the customer how to setup the system, involving minimal manipulations. The assembly should be quick and easy.
The read-out time should be very short. The hardware should sit very comfortably under the user’s arm during that time

## Slide 6: Thermometer Packaging
The total thermometer package to be placed underarm will be lightweight (< 2 lbs) yet mechanically robust
The packaging material will be waterproof, cleanable, and biocompatible

## Slide 7: Power Switch
The system should contain a mechanical switch available to the user that powers up the system
When system powers up, system will immediately seek connection to the nearest iPad

## Slide 8: Communication Protocol
All data will be transmitted via WiFi on a pre-existing network. No other wireless protocols will be available

## Slide 9: Security
Wireless data transmission should only be accessible to the user
Necessary protective measures should be taken to prevent malicious hackers on the network

## Slide 10: Display Requirements
Body temperature data will be displayed in landscape format
The display will contain instantaneous body temperature, average temperature over 1s, and average temperature over 10s
User will have option to switch data display between F and C
Data refresh speed will be 1 Hz

## Slide 11: Error Prevention
If connection is lost, data should be asynchronously invalidated.
If no connection is present, app should not display any data, but rather give an error message

## Slide 12: Audio Output
The user interface app will sound an alarm using the built in iPad speakers when the body temperature is above 90 F to confirm active operation of system

## Slide 13: User Friendly GUI
All data displays should be very clearly marked and easily read by users
There should be no latency dependency on the hardware
Switch between F and C should be purely cosmetic, smooth, and clearly marked (perhaps toggle switch)