## Slide 1: Axillary Thermometer Design Review 1 9/23/14
Team 3: Brian cefali, karman chu, ryan Dougherty, will lenk

## Slide 2: Sensor Schematic

## Slide 3: Arduino Pseudo-Code
Setup()
Enable Serial Port
Begin WiFi comms
Initialize global variables
Loop()
Start tracking run time
If (1 ms elapsed)
sampleData()
Update 1 ms counter
If (data interval elapsed)
sendPacket(inst, avg1, avg10, ID)
Update data interval counter
If (1 s elsapsed )
Clear 1 second average variable
Update 1 second counter

## Slide 4: Arduino Pseudo Code
sampleData()
Read analog pin
Convert analog reading to temperature value
Store reading in model array
increment index counter
If (end of array reached)
calcAverages()
Reset index counter }
Update instantaneous temp
calcAverages()
Iterate through Array
Calculate average
Update next 1 s average
If (average counter = 10)
reset average counter

## Slide 5: iPad Pseudo Code
on_launch():
init_new_viewcontroller() /* done by default? */
init_server_socket()
init_server_socket():
server = create_server_socket()
if server.failed:
update_view(SERVER_FAIL)
on_client_connect(client):
if (already_connected)
client.send(ALRDY_CXND)
else
already_connected = TRUE
establish_link(client)
on_client_disconnect():
already_connected = FALSE
state = clear_reading_history()
state.reason = CLIENT_DISCXN
update_ui(state)

## Slide 6: iPad Pseudo Code
on_wifi_disconnect():
already_connected = FALSE
state = clear_reading_history()
state.reason = WIFI_DISCONNECT
update_ui(state)
on_exit():
close_sockets()
on_recv_reading(reading):
last_reading = parse_reading(reading)
on_1s_pulse():
update_ui(last_reading)
if (!alarm_sounded && last_reading.inst_temp > ALARM_TEMP)
sound_alarm()
alarm_sounded = TRUE
on_cf_btn_click():
swap_cf_display()
on_reset_btn_click():
state = clear_reading_history()
state.reason = HISTORY_RESET
update_ui(state)