## Slide 1: System Breakdown of Axillary Thermometer
Team 3
Karman Chu, Will Lenk, Brian Cefali, Ryan Dougherty

## Slide 2: Block Diagram
Sensor Package
Arduino
Wireless Communication
iPad
Power
Supply Voltage
Supply Voltage
Data
Information
Information
Body Temp
User Input
Information
Display

## Slide 3: Sensor Package
Inputs
  Body Heat
  Power
Outputs
  Analog Voltage
Key Features
  Thermistor sits in wand-shaped foam core enclosure
  Voltage divider circuit outputs analog voltage proportional to body temperature
Foam Core Case
Thermistor
Voltage Divider Circuit
Power In
Analog Voltage Out
Body Temp In

## Slide 4: Power
Inputs
  9V Battery
Outputs
  9V Supply to Arduino, Thermistor
Key Features
  9V snap soldered to proto-board allows user to easily switch battery
  Throw switch on proto-board turns entire system on and off
Arduino
9V Battery
Sensor Package
9V Snap
Switch
Proto
Board
9V Supply

## Slide 5: Arduino
Inputs
  9V Supply
  Data (Analog Voltage)
Outputs
  Information to Wi-Fi Network
Key Features
  Samples Data at 1kHz
  Outputs Information at 1kHz
  Computes Averages
Analog to Digital Converter
Temperature Model
Processing Routine
Dispatcher
(Serial Port)
Setup,
Wi-Fi Shield Handshake
Data
Data
Information
Information Out
Data In
9V Supply

## Slide 6: Wireless Communication
Input
  Information
Output
  Information
Key Features
  Wi-Fi Shield pre-configured to connect to password protected network
Wi-Fi Shield
Router
Information from Arduino
Information to iPad

## Slide 7: iPad
Input
  Information From Router
  User Input
Output
  Visual Display
  Audio Alarm
Key Features
  Displays average and instantaneous temperature
  Display option of Fahrenheit or Celsius
  Sounds alarm when body temperature exceeds 90 F
Temp Listener (Main Loop)
View Controller
Event Processor (Handler)
User Input
Temp Update
Event Data
Information
User Input
Visual Display,
Audio Alarm

## Slide 8
Task | Deadline | Deliverable | Person Responsible
Circuit Design | Tuesday Sep 23 | Complete schematic | Karman, Will
App Design | Tuesday Sep 23 | App Specifications and Layout | Everyone
Circuit Implementation | Thursday Sep 25 | Functional Voltage Divider Circuit with Thermistor | Karman, Will
Integration of sensor with Arduino | Thursday Sep 25 | Arduino connected to sensor; power distribution achieved | Karman, Ryan, Will
Data Processing Using Arduino | Saturday Sep 27 | Arduino program computes, outputs temp values | Everyone
Wireless Communication | Monday Sep 29 | iPad / Arduino communication | Brian, Ryan
Sensor Packaging | Tuesday Sep 30 | Working Sensor in packaging | Ryan, Will
Final App | Tuesday Sep 30 | Working App | Brian, Ryan
Final Assembly | Tuesday Sep 30 | Modules assembled and packaged in final form | Everyone
Final System Prototype | Thursday Oct 2nd | Live Demonstration and Presentation | Everyone