## Slide 1: Digital Thermometer & App: Mission Statement and Project Specifications
EE93/COMP50, Mobile Medical Devices
S. Broner, B. Frizzell, A. Henry, D. Wiegard and E. Wong – September 11, 2014
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAA

## Slide 2: Mission Statement
“Our goal is to develop a patient temperature monitoring system that wirelessly pairs an underarm thermometer worn by the patient with a real-time iPad display to be used by medical personnel by October 2, 2014.”

## Slide 3: Assumptions
Measurements will be taken on a patient wearing a T-shirt or comparable thickness of clothing.
Thermometer only needs to operate in the range of 10 °C to 50 °C.
Final product weight will include an integrated circuit in place of Arduino.
Prototype will be designed to operate as one probe per iPad.

## Slide 4: Temperature Probe
Specification | Value
Temperature | 10 °C < T < 50 °C
Sampling Rate | 1000 ± 10 Hz
Transmission Protocol | IEEE 802.11 (WiFi)

## Slide 5: Temperature Probe (cont’d)
Specification | Value
Battery Life | > 30 minutes while operating.
Analog/Digital Conversion | ≤ 5 ± 0.0049 V
Power Source | 9V battery and 2.1mm AC-to-DC wall adapter will both be supported.

## Slide 6: iPad User Interface
Specification | Value
Temperature Update Rate | 1 ± 0.01 Hz
User Unit Display | °F/°C
Alarm | 65 dB < V < 80 dB
Orientation | Landscape

## Slide 7: iPad User Interface (cont’d)
Specification | Value
Touch Interface | One button functions
Graphical Display | Textual and non-textual information

## Slide 8: Product Encasement
Specification | Value
Weight | < 112 g1
Probe Housing | Thermister will be house in a water resistant case.
Probe Shape | Product should be ergonomic and fit comfortably in the underarm.
Sterilizability | Product should be fully sterilizable.
1Final product intended to use alternative microprocessor.