## Slide 1: Digital Thermometer & App: Hardware & Software Design Review
EE93/COMP50, Mobile Medical Devices
S. Broner, B. Frizzell, A. Henry, D. Wiegard and E. Wong – September 23, 2014
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAA

## Slide 2: System Design
Wifi Network
Therm. Circuit
Arduino
iPad
Alarm LED
Heat Input
Touch Input
On/off
Notes: Arduino communicates unidirectionally to iPad through wifi network
iPad displays pre-processed data
Separation of concerns paradigm

## Slide 3: System Design - Arduino Processing
Wifi Network
Therm. Circuit
Arduino
iPad
Alarm LED
Heat Input
Touch Input
On/off

## Slide 4: System Design - Arduino Processing
Therm. Circuit
Alarm LED
Heat Input
Voltage
Level
0 – 5 V
Arduino
Analog
Input Pin
ADC
Process
Wifi Shield
VHIGH
0 - 1023
On/off

## Slide 5: System Design - Web Serving
Wifi Network
Therm. Circuit
Arduino
iPad
Alarm LED
Heat Input
Touch Input
On/off

## Slide 6: System Design - Web Serving
Wifi Network
Process
Arduino
JSON Conversion
Wifi Shield
Server
(update 1Hz)
Configure IP address

## Slide 7: System Design – iPad display
Wifi Network
Therm. Circuit
Arduino
iPad
Alarm LED
Heat Input
Touch Input
On/off

## Slide 8: System Design – iPad display
Wifi Network
Touch Input
Capacitive Touchscreen
iPad
Wifi
Module
Wifi
Module
C/F Button
Dismiss Button
1 Sec. Avg. View
10 Sec. Avg. View
Inst. View
Alarm Module
Wifi
Module
View Controller
NSData

## Slide 9: Task List
Task | Duration | Deliverable | Team Members
Build and test thermistor circuit | 2 hours | Circuit with 0 – 5 V output | Dave, Sam
Design Arduino sampling code | 2 hours | Arduino sampling at 1kHz | Sam, Alex
Design running average processing | 1 hour | Final three float values, updated at 1kHz | Sam, Alex
Establish wifi connection and host server and implement REST-like functionality | 3 hours | User-specified data accessible from remote browser | Ean, Brad
Design iPad URL calls | 1 hour | User-specified data displayed in Xcode log | Ean, Brad
Create view controller and alarm logic | 2 hours | User-specified data displayed in Xcode simulator and alarm functions properly | Dave, Alex
Design iPad front end display | 1 hour | Intuitive app view with buttons connected to view controller | Brad, Dave, Sam
Deploy app to iPad and test | 3 hours | Full hardware and app ready for demonstration | Team